E-Team Squadra Corse
Introduzione al software

---
Architettura Hardware
- Sensori: temperatura, pressione, velocità (“foniche”), PPS, IMU
- Attuatori: Inverter (+ motore), pompa, contattori HV
- Battery Pack + BMS + IMD
- Vehicle Control Unit (VCU)
- Shutdown Chain (SDC)
- Display, Logging, Telemetria

---
Architettura di Comunicazione
- Uno o più bus di comunicazione basati su protocollo CAN
- EV-A: 3 can bus
  - CAN-S: signal bus, CAN-I: inverter can, CAN-B: BMS CAN
- ET-16: bus unificato (il BMS usa anche un bus interno)
- LoRA per la comunicazione telemetria

---
Software “in-house”
- can_common: generazione DBC, bindings C, documentazione, analisi del carico del bus
- can_bootloader: STM32 and AVR
- config_lib: configurazione dei parametri senza ricompilare
- etdv_dashboard: visualizzazione
- Telemetria: CAN2Radio, Radio2CAN
- Firmware MCU

---
Software utilizzato
- Git/Github per il controllo di versione e collaborazione
- PlatformIO: programmazione dei micro
- Meson e Cmake: compilazione su linux
- STM32CubeMX: Configurazione degli STM32 (VCU)
- FreeRTOS: scheduler real-time che gira sulla VCU
- cantools, asammdf, can-utils
- Linux (sviluppo e raspberry)

---
CAN Bus Design

---
Design space
CAN bus speed: as high as 1Mbit/s (up to 40m cable length). Higher speed is associated to less noise immunity.
Can Messages (Standard Frame):
ID (11bit)
Payload (up to 8 bytes)
Message Period
Lower ID means higher priority.
Affects worst case message delay.
Affects bus utilization and worst case delay of lower-priority messages.
Affects total transmission time (MCU)
Affects bus utilization

---
Design example

---
can_common
Python based, generates a bunch of stuff:
- DBC for reading the CAN bus
- C bindings to automate packing/unpacking messages
- Bus documentation in PDF
- Bus load and timing analysis

---
using can_common to describe the bus
can_def.py
vcu_messages = [
    {
        'name': 'iq_cmd',
        'senders': [NodeId.VCU],
        'receivers': [NodeId.INVERTER],
        'message_id': MsgId.IQ_CMD,
        'comment': 'Quadrature current command',
        'cycle_time': None,
        'signals': [
        {
        'name': 'iq_rms',
        'scale': 0.1,
        'range': (0, 200),
        'unit': 'Arms',
        'comment': 'RMS value of quadrature current',
        },
        ]
    },
    ...

---
Generating the DBC and bindings
 1 from dbc_dict_processor import create_dbs, fail_on_overlapping_ids
 2 from dbc_bindings_generation import write_dbc_files, write_nodes_header
 3 from can_def import main_messages, NodeId, DBC_VERSION
 4 import cantools
 5
 6 main_db, main_bindings_db = create_dbs(main_messages(), NodeId, NodeId, DBC_VERSION)
 7 fail_on_overlapping_ids([main_db])
 8 cantools.database.dump_file(main_db, r'dbc/main.dbc')
 9
10 write_dbc_files(main_bindings_db, 'main', 'bindings/main_db.h', 'bindings/main_db.c')
11
12 write_nodes_header([
13 ('main', DBC_VERSION, NodeId),
14 ], 'bindings/nodes.h')

---
Firmware development
Concepts and tools

---
HAL (Hardware Abstraction Layer)
- Abstracts hardware details from implementation
  - CAN sending/receiving, sensor reading, pin control, timers, etc.
- Allows simulating the firmware code on a Linux PC (posix_hal)
- Used by almost all our firmwares (VCU, sensorboard, pdu)

---
HAL for design example SB
 1 #pragma once
 2
 3 #include <stdbool.h>
 4 #include <stdint.h>
 5
 6 bool hal_can_init();
 7 extern bool hal_send_can_message(uint32_t addr, const uint8_t* data, uint8_t length);
 8 extern void hal_handle_can_message(uint32_t addr, const uint8_t* data, uint8_t length);
 9
10 extern void analog_sensor_conversion_ready(int num_sensor, float value);
11
Called from interrupt on real hardware

---
VCU HAL

---
Scheduling periodic tasks
- Simple approach: use a timer (fake_bms, sensorboard, pdu)
- When more control is needed, use a RT scheduler/OS (e.g. FreeRTOS)

---
Heartbeats
- Periodic signals (usually CAN messages) generated by a board to signal it is alive
- Usually has some info attached (state, faults etc)
- Choose the period by estimating needed response time to a fault
- Some commands need to be issued periodically to be valid, e.g. inverter control or BMS command

---
Critical Signals and CRC
- Critical signals are valid only if their last updated value is recent enough
- Example: PPS (pedal position signal) needs to be updated at a fast enough rate (15ms~20ms period) to ensure safety
- For stronger safety, CAN messages can have an additional CRC of few bits to check message intentionality (assuring that another board is not writing a message with wrong id)
- To ensure message ordering, add a rolling counter field to the payload

---
VCU Critical Signals
Updating a critical signal (done in the can handler task):
Reading a critical signal: if value was not updated, dest value is garbage. Must either fail or provide an alternative safe value (e.g. 0 PPS)

---
State Machines
- Communicate design intent to others
- Reason about correctness
- Validation and code generation from state machine definitions is common in automotive (see Simulink + Stateflow)
- See VCU State Machine

---
CAN bootloader
- Inspiration for the protocol from an AVR doc example/technical note
- Lives in a sector of the flash
- Each board has a unique identifier for flashing
[env:can_bootloader]
build_type = debug
can_baudrate=500000
canbl_id=0x06
canbl_node=0x02
Bootloader config is embedded in the platformio env.
Upload using
pio run -t can_upload_stm32

---
config_lib
- Somewhat similar to standard XCP protocol for ECU
- Discoverable parameters with descriptions and bounds
- Supports bool, float, int datatypes
- Forward compatible storage on flash if used correctly
- Has a GUI… improvements or rewrites are welcome

---
PlatformIO tips
- Use environments to have different configurations for the same project (e.g. different build time flags/options)
- Can be used in vscode, but try to use it with the command line at least a couple of time

---
Firmware testing
- Unit testing: testing the single functions (see platformio documentation)
- Functional testing: testing of the functionality of a software unit (e.g. one particular firmware)
- Integration testing: testing the interaction between two ore more components (e.g. testing the whole firmware)

---
Reproducible Testing
My attempt: ETeam Test Framework
 1 def test_vcu_precharge_missing_signals(logging_manager):
 2 mgr = logging_manager.with_can_dispatcher(vcu=True)
 3 precharge_start = 3
 4 total_time = precharge_start + 5
 5
 6 # create the following bms states sequence:
 7 # montoring -> precharge -> error
 8 bms_status_signal = mgr.main_can_signal("bms_BMS_Status.BmsMasterStatus")
 9 bms_status_signal.set_values(
10 [0, precharge_start, precharge_start + 3, total_time],
11 [
12 "eFsmState_STANDBY",
13 "eFsmState_PRECHARGE",
14 "eFsmState_OPERATIONAL_LOAD",
15 "eFsmState_OPERATIONAL_LOAD",
16 ],
17 )
19 # ts button press for ~3 seconds
20 button_press_signal = mgr.main_can_signal("STEERING_WHEEL_ButtonInputs.buttons")
21 button_press_signal.set_value(0.2, 1)
22 button_press_signal.set_value(precharge_start + 1, 0)
23
24 mgr.set_main_can_signals(bms_status_signal, button_press_signal)
25 logs = mgr.run(total_time)
26
27 vcu_status_signal = logs.select(mgr.main_bus_name).extract_signal(
28 "VCU_VCU_Heartbeat.Status"
29 )
30
31 assert (
32 vcu_status_signal.predicate(lambda s: s == "IDLE" or s == "PARAM_UPDATE")
33 .always()
34 .eval()
35 )

---
Vehicle Model/Simulator
- el_vehicle_model: C++ implementation of a vehicle model (dynamics, powertrain, some control electronics)
- Preliminary support for export as FMU (Functional Mock-Up Unit), which can be used inside Simulink or Modelica
- Works alongside the other simulated firmwares, so structure needs to be coded directly in (C++, boost, not really easy)

---
Homework: design example
- Control the fan speed to regulate the heatsink outflow and keep the inverter under 90 C
- Max power to dissipate: 70kW * 0.05
- Water temperature is measured

---
???
The value of Rfan must be controlled indirectly using VCU CAN messages

---
Homework: design example
- Control the fan speed to regulate the heatsink heatflow and keep the inverter under 90 C
- Max power to dissipate: 70kW * 0.05
- Water temperature is measured
- Thermal model simulator is already there, follow README for compilation and further instruction
- VCU pps signal should be critical, fix the bug!
- Sensorboard code for temperature reading is missing!